## Slide 1: HLS LabA Design Optimization
Matrix Multiplication
2022/03/30

## Slide 2: Outline
Original code explanation
Optimized code explanation
Performance analysis
Tradeoff

## Slide 3: Original code explanation
Row
b
res
x
=
Col
a
Notes: 計算矩陣a和矩陣b相乘，把結果存到矩陣res，總共使用三層for迴圈，第一層for是選擇矩陣a的row，第二層for是選擇矩陣b的col，之後先把輸出res[i][j]給歸零，最後用第三層for累加a[i][k]×b[k][j]。
根據上圖的程式碼，可以知道矩陣相乘的順序如下圖，沒有使用pragma，輸入與輸出的讀寫重複次數太多，雖然面積比較小，但是比較慢，這是一個可以改進的方向。

## Slide 4: Optimized code explanation
ARRAY_RESHAPE
  New array with fewer elements but with greater bit-width
a
b
  Bit-width from 8-bit to 24-bit

## Slide 5: Optimized code explanation
INTERFACE ap_fifo
  Enable steam data transfer

## Slide 6: Optimized code explanation
PIPELINE rewind
  No pause between loops

## Slide 7: Optimized code explanation
Cache input data
  Red: first read
  Blue: data reuse

## Slide 8: Optimized code explanation
Write once
  Red: write to tmp
  Blue: write to res

## Slide 9: Performance analysis
 | Latency | Interval | DSP | FF | LUT
Lab1 | 24 | 25 | 2 | 117 | 393
Lab2 | 14 | 9 | 2 | 243 | 543
ARRAY_RESHAPE | 15 | 16 | 6 | 248 | 367
ap_fifo | 33 | 34 | 2 | 62 | 201
ARRAY_RESHAPE + ap_fifo | 23 | 24 | 6 | 172 | 289
rewind | 23 | 18 | 2 | 162 | 405
cache | 24 | 25 | 2 | 239 | 667
Loop_flatten | 18 | 19 | 6 | 441 | 472
Red is min, blue is max.

## Slide 10: Tradeoff
For FPGA hardware, 3x3 matrix multiplication utilizes ~0%.
Use the fastest one: Optimized code from Lab2
  ARRAY_RESHAPE
  INTERFACE ap_fifo
  PIPELINE rewind
  Cache input data
  Write once

## Slide 11: Thank you!
hsu880105/HLS_LabA_Design_Optimization (github.com)